## Slide 1: FIR filter and Distributed Arithmetic
Dr Koushik Maharatna
University of Southampton

## Slide 2: Multiply-Accumulate is a common function
The generalised form of MAC operation is
Where, xk is the incoming data at kth time instant, yk is the output, hk are certain fixed values
Occurs every now and then in signal processing
A very prominent example is Finite Impulse Response (FIR) and Infinite Impulse Response (IIR) Filters
Typically we find out the filter co-efficients (hk) based on the filter characteristics we want – normally using Matlab or other software - and then implement it

## Slide 3: FIR filter
The basic equation of Nth order FIR filter is
This is the direct form of implementation of an FIR filter
Lots of multiplications and additions are happening here
How to implement such a structure?

## Slide 4: FIR filter
Let’s try to understand it a bit more: let’s say we are dealing with a 3rd order FIR filter
h0, h1, h2, h3 are 2, 3, 4 and 5 respectively
At t = 0, x0 = 1; y0 =(2*1+0+0+0) = 2
At t = 1, x1 = 2; y1 = (2*2+3*1+0+0) = 7
At t = 2, x2 = 3; y2 = (2*3+3*2+4*1+0) =16
At t = 3, x3 = 4; y3 = (2*4+3*3+4*2+5*1) =30
There are different ways to implement such a filter, e.g. consult the multiplier.pptx to see how a multiplier with one fixed multiplier can be realised using shift-and-add techniques
You may also consider Distributed Arithmetic technique we describe here

## Slide 5: Distributed Arithmetic (DA)
Let’s say xn is the nth data and is a k-bit number. So…..
REMEMBER xn,i is either 0 or 1
Let’s take it term by term

## Slide 6: Distributed Arithmetic (DA)
Rearranging we get
Since hi’s are fixed and xn,i are either 0 or 1, each term in the [.] becomes only a combination of hi depending upon the value of xn,I and therefore can be precomputed and stored in a LUT
Once we have the actual xn’s we can use their bit patterns as address to retrieve the correct values from the LUT and send it to sum block
What we achieved here is very fast multiplierless multiplication operation
Let’s explain it with a specific example

## Slide 7: Distributed Arithmetic (DA)
h0, h1, h2, h3 are 2, 3, 4 and 5 respectively, xn is a 4-bit number and n = 4
]+ ]+ ]+ ]
] + ] + +
Put all 2* terms together

## Slide 8: Distributed Arithmetic (DA)
So we get
+ + * +
Now we need to make a co-efficient table: basically that will describe all possible bit combination of xn and the corresponding coefficient to calculate Sum*
We will need 2n length coefficient table and therefore in the present case we will need 24 length table
Let’s make it…… you need to keep an eye on the last equation of the last slide

## Slide 9: Distributed Arithmetic (DA)
X0,k | X1,k | X2,k | X3,k | Coefficient
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | h3 = 5
0 | 0 | 1 | 0 | h2 = 4
0 | 0 | 1 | 1 | h2+h3 = 5+4 = 9
0 | 1 | 0 | 0 | h1 = 3
0 | 1 | 0 | 1 | h1+h3 = 3+5 = 8
0 | 1 | 1 | 0 | h1+h2 = 3+4 = 7
0 | 1 | 1 | 1 | h1+h2+h3 = 3+4+5 = 12
1 | 0 | 0 | 0 | h0 = 2
1 | 0 | 0 | 1 | h0+h3 = 2+5 = 7
1 | 0 | 1 | 0 | h0+h2 = 2+4 = 6
1 | 0 | 1 | 1 | h0+h2+h3 = 2+4+5 = 11
1 | 1 | 0 | 0 | h0+h1 = 2+3 = 5
1 | 1 | 0 | 1 | h0+h1+h3 = 2+3+5=10
1 | 1 | 1 | 0 | h0+h1+h2 = 2+3+4 = 9
1 | 1 | 1 | 1 | h0+h1+h2+h3 = 2+3+4+5 = 14

## Slide 10: Distributed Arithmetic (DA)
Now let’s see how it works
Let x0 = 10 = 1010
x1 = 12 = 1100
x2 = 15 = 1111
x3 = 11 = 1011
y = 2*10+3*12+4*15+5*11 = 171
x0,0 = 0, x1,0 = 0, x2,0 = 1, x3,0 = 1; Sum0 = 9
x0,1 = 1, x1,1 = 0, x2,1 = 1, x3,1 = 1; Sum1 = 11
x0,2 = 0, x1,2 = 1, x2,2 = 1, x3,2 = 0; Sum2 = 7
x0,3 = 1, x1,3 = 0, x2,3 = 1, x3,3 = 1; Sum3 = 14
y = Sum0*20 + Sum1*21 + Sum2*22 + Sum3*23 = 9 +11*2 +7*4+14*8 = 171

## Slide 11: Implementation
Serial implementation: LSB first
x0,3
x0,2
x0,1
x0,0
x1,3
x1,2
x1,1
x1,0
x2,3
x2,2
x2,1
x2,0
x3,3
x3,2
x3,1
x3,0
Address bus
Coefficient table
+
Variable shifter
Counter
Result out
Variable shifters are wire-dominated circuits

## Slide 12: Implementation
Serial implementation: MSB first
x0,0
x0,1
x0,2
x0,3
x1,0
x1,1
x1,2
x1,3
x2,0
x2,1
x2,2
x2,3
x3,0
x3,1
x3,2
x3,3
Address bus
Coefficient table
+
1-bit shifter
Result out

## Slide 13: Implementation
Parallel implementation